## Slide 1: MTB Handbook
Chris Styles
V1.0

## Slide 2: MTB Handbook
Overview
DAPlink
Module Carrier
Onboard peripherals
Grove connectors
Loopback testing

## Slide 3
Overview

## Slide 4: Overview
Potentiometer
Button
DAPLink Micro USB
I2C Temperature sensor
I2C bus select
128 x 32 LCD
DAPLink Power switch
DAPLink Reset
Grove Voltage selector
DAPLink LEDS
Grove Sockets
Module Carrier Socket

## Slide 5
DAPLink

## Slide 6: DAPLink
LPC 11U35
USB Serial (stdio)
USB MSC (Drag and drop)
USB HID (Debug)
Module
SWCLK/SWDIO
nRESET
TGT_TX / TGT_RX
Updating the DAPLink firmware:
Plug in your MTB, holding down the reset button, a drive called CRP Disabled will enumerate
Open the drive, and delete the file called "firmware.bin"
Copy the required .bin file onto the "CRP Disabled" drive.
  On Windows, simply drag and drop the file
  On Linux/Mac, use command: dd if={new_firmware.bin} of={firmware.bin} conv=notrunc
Disconnect and reconnect the MTB, it should now enumerate as drive called “DAPLink”
Note : For drag and drop programming to work, the correct .bin files has to be used, as it will need ot contain the flash algorithm for the target device

## Slide 7
Module Carrier

## Slide 8
GND
3v3
VBUS
SWDIO
SWCLK
nRESET
TGT_TX
TGT_RX
TX1
RX1
SDA1
SCL1
MOSI1
MISO1
SCK1
GP0
GP1
AIN0
AIN1
AIN2
GND
GP8
TGT_RTS
GP7
GP6
GP5
GP4
TGT_CTS
TX2
RX2
SDA2
SCL2
MOSI2
MISO2
SCK2
GP3
GP2
PWM2
PWM1
PWM0
DAPLink
DAPLink
SD / LCD / GROVE
Button
Pot
Grove
Grove
GROVE / Onboard
LCD : A0
LCD : nRST
LCD : nCS
Red LED
Blue LED
Green LED
3v3 @ 250mA
GROVE / Onboard
GROVE
GROVE
SD : nCS
GROVE

## Slide 9
Onboard peripherals

## Slide 10: Onboard peripherals : LCD
128 x 32 LCD
MOSI1
MISO1
SCK1
GP7
GP6
GP5
A0
nRST
nCS
SPI

## Slide 11: Onboard peripherals : SD Card
Micro SD
MOSI1
MISO1
SCK1
GP2
nCS
SPI

## Slide 12: Onboard peripherals : I2C devices
LM75B Themometer
Addr : 0x90
SDA2
SCL2
SDA1
SCL1
AT24LC256 EEPROM
Addr : 0xA0
I2C bus select
SCL/SDA

## Slide 13
Grove Connectors

## Slide 14: Grove connectors
TX1
RX1
SDA1
SCL1
MOSI1
MISO1
SCK1
TX2
RX2
SDA2
SCL2
MOSI2
MISO2
SCK2
GP3
GP2
AIN1
AIN2
CON1
CON2
CON3
CON4
CON7
CON5
CON6
CON8
VCC_GROVE
3.3v
5v
Grove voltage selector

## Slide 15
Loopback testing

## Slide 16: Loopback testing
To reuse the basic tests written for the “CI Sheild”